## Slide 1: Pre-existing Vascular Access Device (PVAD)

## Slide 2: Pre-existing Vascular Access Device (PVAD)
A venous catheter inserted into a central vein (without valves) to provide direct access to the patient’s vascular system. The distal end of the catheter is usually located in the superior vena cava.
Notes: The catheter usually is “heparinized” so flushing is necessary.

## Slide 3: Why are they used ?
Patients with chronic serious medical conditions
PVAD’s provide vascular access through a synthetic tube that is inserted beneath the skin
  Consistent pathway for
    Medication
    nutrient administration
    Dialysis
    Blood withdrawal.
This device spares patients the repeated pain/discomfort of “searching” for peripheral venous access and needle sticks.

## Slide 4: Types - External
External Access - A tube can be seen sticking out of the patient
  Short-Term single or multi-lumen catheter
  Peripheral inserted central catheter (PICC)
  Hickman catheter
  Broviac catheter
  Groshong catheter
Accessible by PMs

## Slide 5: External Access Devices
Patients with these devices come in all age ranges
Many are immunosuppressed because of treatments for their disease process

## Slide 6: Multi-Lumen
Notes: Hickman Catheter

## Slide 7: Hickman Catheter
Notes: Most external lines that patients are allowed to go home with are inserted into the venous system.

## Slide 8: Types - Internal
Internal Access:
  Implanted ports
  Fistulas
NO tube can be seen on patient’s skin exit site
NOT accessible by PMs

## Slide 9: Internal Access Devices
Any access that is subcutaneous and requires access through the skin
NOT to be accessed by prehospital personnel
Notes: Internal access devices are difficult to access by trained individuals. If you are unsure of the device ask a bystander or guidance from the hospital.

## Slide 10: When May You Access a PVAD?
Cardiopulmonary arrest
Extremis due to circulatory shock
Base Hospital discretion
Notes: Before accessing any device, the provider should be clear on the device they are accessing. At no time should you access a device that is connected to an artery.

## Slide 11: WHY might you access a PVAD?
Administration of IV fluids
  Normal Saline
Administration of all IV route medications

## Slide 12: What Could Go Wrong?
Infection
Air embolism
Thrombosis
Catheter damage
Notes: Reported problems in literature
Infection (3-60%)
Air Embolism (Rare)
Thrombosis (4-10%)

## Slide 13: Common Causes of Infection
Failure to maintain aseptic technique
Immunosuppressed patient
Irritated suture line
Failure to comply with routine dressing change care

## Slide 14: Infection Prevention
Hand washing or use of an alcohol based hand gel.
Use STERILE gloves at all times when handling the catheter injection port.
Prep the injection port with an alcohol swab twice (x2).
Obtain new gloves or supplies if they become contaminated.
Notes: Remember do no harm. Infection prevention will help improve patient outcome.

## Slide 15: Air Embolism
Introduction of air into the circulatory system.
Since the PVAD provides a direct line into the central circulation, the introduction of air into these devices can be very hazardous.

## Slide 16: Air Embolism Signs/Symptoms
Sudden respiratory distress
Decreased blood pressure
Weak pulse
Sudden change in LOC Immediately place the patient in left lateral Trendelenburg position and clamp catheter should this occur.

## Slide 17: Air Embolism Prevention
DO NOT remove injection cap from catheter.
Insure the catheter is clamped after use.
DO NOT allow IV fluid to run dry.
ALWAYS expel air from preload syringe prior to administration.

## Slide 18: PVAD Thrombosis
A blood clot within the vascular system caused by improper handling and/or maintenance of the PVAD.
Dislodgement of this clot can cause vascular damage and/or a pulmonary embolus.

## Slide 19: Thrombosis Signs/Symptoms
Mild to Moderate neck pain
Ipsilateral swelling of the arm, neck and face
Fever, malaise
Inability to aspirate blood through catheter

## Slide 20: Thrombosis Prevention
If resistance is met, DO NOT force medications or fluid through catheter.
Follow medication administration with at least a 5 ml Normal Saline flush.

## Slide 21: Catheter Damage
Damaged catheters are no longer a benefit to the patient and could be potentially harmful.
If damage should occur, immediately clamp catheter between damaged area and skin exit site with padded hemostats.
Notes: Care should always be taken when working with these devices. Although intended for multiple uses for a long period of time rough handling could cause damage and the need for replacement.

## Slide 22: Needleless Systems
Most needless systems will work with these devices.
Avoid using small syringes since they tend to create too much pressure in the catheter, which can cause the catheter to collapse or rupture. 10ml syringe works the best

## Slide 23: Blood Withdrawal
Although most of these devices have the ability to withdraw blood for diagnostic tests, some recommend against withdrawing blood samples.
Blood samples are NOT to be withdrawn from a PVAD by prehospital personnel.
Notes: For simplicity and less confusion this is the recommended policy for prehospital use.
Broviac catheters because of size should not be used for blood withdrawal
Groshong catheters tend to kink more or tear with frequent blood withdrawals.